## Slide 1: The World’s Most Advanced Ozone Technology
Philippe Taliana – Global Sales Manager

## Slide 2: Typical Ozone System Process Diagram
System Components
  Oxygen Supply:
    Liquid Oxygen (LOX) or
    Onsite generation (PSA / VSA) or delivered oxygen for feed to ozone generator
    Min Quality: >93% O2 @ Dewpoint = -65°F
  Ozone Generator:
    Converts O2 to ~10% O3 (typ) using electrified plasma field
    Pinnacle generators offer constant %BW output at any turn-down
    Market Leading Energy Efficiency (3.5 kWh/lb)
  Water Chiller:
    Closed-loop cooling for ozone generator
    Glycol based fluid preserves unit efficiency
  O3 Injection
    Dissolves O3 Gas Into Solution for Reaction
    Custom Design (based on dose, flow, etc)
    Typical Transfer Efficiency >93%
  O3 Destruct
    Captures un-dissolved O3 gas to prevent exposure
    Autocatalytic Reaction w/ Monitoring
    Assures no release / exposure to O3
O2 Supply (PSA, VSA, or LOX)
O3 Generator
Water Chiller
Reactor / Holding / Contact Tank
O3 Destruct
Filtered Effluent
Typical Pinnacle Scope of Control
O3 Injection

## Slide 3: Modular Generator Cells
The World’s Most Advanced Ozone Generator Technology
  Developed as the world’s most energy efficient ozone technology
  Completely Integrated / Standalone Ozone Generator Cells
  Ruggedized Service-Free Cell Design
  Advanced Materials, Power Supply & Controls Technology
Integrated Controls — individual optimization & monitoring of each ozone cell
Ruggedized Construction — immune to vibration & shock
Advanced Materials — Ceramic Dielectrics and Maintenance-Free Operation
Built-In Hi-Frequency PSU — virtually silent 23 kHz operation
Dual Air / Water Cooling — reduces cooling by 40-60%
Constant %BW Output — 0-100% turn-down via variable gas-flow operation
Industry Leading Efficiency — 3.5 kWh/lb operation
1
2
3
4
5
6
7

## Slide 4: Pinnacle Ozone Technology
A Family of Ozone Generator Platforms
  Family of Flexible / Modular Ozone Process Integration Platforms
  Standard Complete Ozone Process Control & Integration
  Specifically Designed to Address 20-600 ppd Target Market
PEAK
SUMMIT
ZENITH

## Slide 5: Scalability
Common QuadBlock / 10X -12X Rack Design Common to ALL Platforms
Modular Enclosure and Pedestal Allows Flexible Design
Only Dimensions & Connection Sizes Change
Common Generator Design & Equipment for ANY Scale!
5x, 10x, 12x
2 x 10 (20x)
3 x 10 (30x)
3 x 12 (36x)
Common 10x/12x Platform
Common 10x/12x Manifold Design
Common PLC Package
Modular Enclosure System
Common / Custom I&C Package
Modular Rack / Platform
Common Inverter / Power System
Platform (Capacity) Specific Connections

## Slide 6: The World Most Advanced Ozone Technology
Modular
  Family of Modular Ozone Process Platforms
  Flexibly Adapts Capacity to Meet Project Needs
  Fully Integrated O3 Process Controls & Instrumentation
  Built-In Multi-Mode Process Control
  Self-Optimizing Process
Reliable
  Zero-Maintenance Ozone Cells
  +25yr QuadBlock Ozone Cell Life
  Built-In Redundancy
  Auto-Compensating Performance
  100% US Made & Supported
24-7 Remote & Online Support
  Onsite Service
Efficient
  Constant 6-18 %BW at Any Output
  True 0-100% Turn-Down
  Industry Leading Power Efficiency
  Less Cooling
  Smaller Footprint
  Ultra-Quiet Operation
  Built-In Cooling / Heating (no HVAC required)
  Appliance Like Installation (5 connections)
  10-40% Lower OPEX and 20yr NPV
Customer Goal: “Like the Results. Love the Equipment”
Market Goal: Establish the New Standard for Ozone Technology

## Slide 7: Quadblocks in a system

## Slide 8: Easy to install
Enclosed cabinets
All equipment is on skids
6 connections:
  Gas in & out
  Water in & out
  Power
  Compressed air.

## Slide 9: Ozone cooling
Different options:
  Air-to-water cooling
  Water-to-water cooling
  Heat Exchanger

## Slide 10: Ozone cooling
Air cooling for the electronics
Water cooling for the Dielectrics

## Slide 11: Oxygen treatment
Manifold
  Donaldson filter
  Demister
  pressure

## Slide 12: Oxygen supply
LOX
  High purity
VSA/PSA
  Min 93%
  Compressor/blower is the maintenance heavy equipment

## Slide 13: Ozone Off Gas Destruct
Ozone destruct sizing:
  Gas production
  Dimension of contact tank
  Level variation in the tank

## Slide 14: Injection
Side Stream injection
Venturi mixing
MTE warrantee (how to measurable?)
Dissolution
  Jet nozzle
  Pipe injection
  Ceramic diffusers

## Slide 15: Instrumentation & controls
MOCP – Master Operator Control Panel
Ozone Generator
  Schneider PLC M251. Allen Bradley available upon request
  HMI Red Lion 15"
External instrumentation:
  Dissolved O3 residual analysers
  Ambient O2 and O3 analysers
  Demister
  Mass flow controler
  Dissolved ozone analyser or ORP

## Slide 16: Project considerations
Equipment availability and lead-times Submittals: 6 weeks
                Delivery: up to 22 weeks after approval
Recommended useful Life/mechanical warrantee Injection can be longer
Performance warrantee
  Output (ppd) warrantee vs MTE

## Slide 17: Local support
Local reps thruout North-America
Service capability out of Cocoa, FL
  Service contracts available
Remote access to the PLC, generators and ancillary components
  95% of the problems can be solved remotely
Your Rep Logo

## Slide 18: Maintenance & Operation
There is no spares to change periodically in the Pinnacle generator.
The dielectrics are built for life. Warrantee for 20 years
Items to maintain regularly:
Pumps on the injection system
Blower on the destruct system
Pumps on the chiller system
Compressor/Blower on O2 generation system

## Slide 19: Applications - Municipal
Disinfection
  Multiple dosing points
Color Removal
Taste & Odor
1-4 Dioxane (AOP)
H2S removal
Leachate
  Color removal
  Bacteria oxydation
Water Body remediation
Ozone & nanobubbles ??

## Slide 20: Applications-Industrial
Aquaculture
  Life support
  Disinfection
  Waste-Water
  Inlet (algea-blooms)
Textile
  Color removal
F&B
  Color Removal
  BOD removal

## Slide 21: Pinnacle Capabilities
Uniquely Capable & Qualified for Ozone Technology Projects
World-Class Customer Support
Single-Source Scope of Supply
In-House Manufacturing
Dedicated Ozone R&D Laboratory
Ozone Application Engineering

## Slide 22: Installations
EXPERIENCE SUMMARY
  20+ Yrs Ozone Experience
  460+ Global Systems
  380+ US Ozone Projects
  50+ Installations
  Ranked #2 Global O3 Supplier by a Fortune 100 Customer
  Participation in All Key Market Segments

## Slide 23: North Burleigh WTP, ND
2.5 MGD MF-RO WTP
  Raw Water Pre-Treatment
  Finished Water Disinfection
Complete Ozone Scope
  Peak 120 ppd System
  O2+Injection+Controls
Overall 20-40% OPEX Savings
>40,000+ Hrs Maintenance-Free beyond calibrations

## Slide 24: Ville de Becancour WTP, QC
2.5 MGD MF-RO WTP
  Raw Water Pre-Treatment
  Finished Water Disinfection
Complete Ozone Scope
  2x Peak 120 ppd System
  O2 + Injection + Destruct
  Complete Process Controls
April 2011 Startup

## Slide 25: City of Sherbrooke, QC
3x Summit 220 ppd System.
Completely Auto Operation (flow & dose pacing / sequencing)
Primary Disinfection
Running since 4th day of Startup

## Slide 26: City of Sanford, FL
1 x 600 ppd
LOX, O3, cooling, injection, controls
DBP Control

## Slide 27: City of Abilene, TX
1 x 300 ppd System
O3 Injection + Destruct + Controls
6000 gal LOX System Supply
March 2015 Startup

## Slide 28: Palm Coast, FL
2 x 200 ppd Muni WTP
0-25 mg/l for UF/NF Concentrate Color / Fe Removal
VSA O2, O3, Cooling Water, Injection, DOZ + Color Control
February 2015 Startup

## Slide 29: Fayetteville, AR
2 x 292 ppd Muni WWTP Disinfection
Partnered with BlueInGreen™ to provide turn-key ozone process solution