## Slide 1
The World’s Most Advanced
Ozone Technology
PINNACLE OZONE SOLUTIONS
Philippe Taliana
GLOBAL SALES MANAGER
OXYGEN SUPPLY
Liquid Oxygen (LOX) or
Onsite generation (PSA / VSA) or delivered oxygen for feed to ozone generator
Min Quality: >93% O2 @ Dewpoint = -65°F
O3 GENERATOR
Converts O2 to ~10% O3 (typ) using electrified plasma field
Pinnacle generators offer constant %BW output at any turn-down
Market Leading Energy Efficiency (3.5 kWh/lb)
WATER CHILLER
Closed-loop cooling for ozone generator
Glycol based fluid preserves unit efficiency
O3 INJECTION
Dissolves O3 Gas Into Solution for Reaction
Custom Design (based on dose, flow, etc)
Typical Transfer Efficiency >93%
O3 DESTRUCT
Captures un-dissolved O3 gas to prevent exposure
Autocatalytic Reaction w/ Monitoring
Assures no release / exposure to O3
Typical Ozone System Process Diagram

## Slide 2
The World’s Most Advanced
Ozone Technology
Philippe Taliana
GLOBAL SALES MANAGER
OXYGEN SUPPLY
Liquid Oxygen (LOX) or
Onsite generation (PSA / VSA) or delivered oxygen for feed to ozone generator
Min Quality: >93% O2 @ Dewpoint = -65°F
O3 GENERATOR
Converts O2 to ~10% O3 (typ) using electrified plasma field
Pinnacle generators offer constant %BW output at any turn-down
Market Leading Energy Efficiency (3.5 kWh/lb)
WATER CHILLER
Closed-loop cooling for ozone generator
Glycol based fluid preserves unit efficiency
O3 INJECTION
Dissolves O3 Gas Into Solution for Reaction
Custom Design (based on dose, flow, etc)
Typical Transfer Efficiency >93%
O3 DESTRUCT
Captures un-dissolved O3 gas to prevent exposure
Autocatalytic Reaction w/ Monitoring
Assures no release / exposure to O3
Typical Ozone System Process Diagram
PINNACLE OZONE SOLUTIONS
Modular Generator Cells
Developed as the world’s most energy efficient ozone technology​
Completely Integrated / Standalone Ozone Generator Cells​
Ruggedized Service-Free Cell Design​
Advanced Materials, Power Supply & Controls Technology
Integrated Controls — individual optimization & monitoring of each ozone cell​
Ruggedized Construction — immune to vibration & shock​
Advanced Materials — Ceramic Dielectrics and Maintenance-Free Operation
​Built-In Hi-Frequency PSU — virtually silent 23 kHz operation
​Dual Air / Water Cooling — reduces cooling by 40-60%
​Constant %BW Output — 0-100% turn-down via variable gas-flow operation
​Industry Leading Efficiency — 3.5 kWh/lb operation

## Slide 3
Modular Generator Cells
THE SUMMIT
10X
12X
THE ZENITH
20X
30X
THE APEX
36X
THE PEAK
5X
A Family of Ozone Generator Platforms
PINNACLE OZONE SOLUTIONS
Developed as the world’s most energy efficient ozone technology​
Completely Integrated / Standalone Ozone Generator Cells​
Ruggedized Service-Free Cell Design​
Advanced Materials, Power Supply & Controls Technology
Integrated Controls — individual optimization & monitoring of each ozone cell​
Ruggedized Construction — immune to vibration & shock​
Advanced Materials — Ceramic Dielectrics and Maintenance-Free Operation
​Built-In Hi-Frequency PSU — virtually silent 23 kHz operation
​Dual Air / Water Cooling — reduces cooling by 40-60%
​Constant %BW Output — 0-100% turn-down via variable gas-flow operation
​Industry Leading Efficiency — 3.5 kWh/lb operation

## Slide 4
A Family of Ozone Generator Platforms
THE SUMMIT
10X
12X
THE ZENITH
20X
30X
THE APEX
36X
THE PEAK
5X
PINNACLE OZONE SOLUTIONS
Common QuadBlock / 10X -12X rack design common to ALL platforms ​
1
Only dimensions & connection
sizes change
2
Modular enclosure and pedestal allows flexible design
3

## Slide 5
Common QuadBlock / 10X -12X rack design common to ALL platforms ​
1
Only dimensions & connection
sizes change
2
Modular enclosure and pedestal allows flexible design
3
Scalability
THE SUMMIT
10X
12X
THE ZENITH
20X
30X
THE APEX
36X
THE PEAK
5X
  Family of Modular Ozone Process Platforms​
  Flexibly Adapts Capacity to Meet Project Needs​
  Fully Integrated O3 Process Controls & Instrumentation​
  Built-In Multi-Mode Process Control​
  Self-Optimizing Process
MODULAR
  Zero-Maintenance Ozone Cells​
  +25yr QuadBlock Ozone Cell Life​
  Built-In Redundancy​
  Auto-Compensating Performance​
  100% US Made & Supported
RELIABLE
  Constant 6-18 %BW at Any Output​
  True 0-100% Turn-Down ​
  Industry Leading Power Efficiency​
  Less Cooling​
  Smaller Footprint​
  Ultra-Quiet Operation​
  Built-In Cooling / Heating (no HVAC required)​
  Appliance Like Installation (5 connections)​
  10-40% Lower OPEX and 20yr NPV
RELIABLE
  Onsite Service
24-7 REMOTE & ONLINE SUPPORT

## Slide 6
  Family of Modular Ozone Process Platforms​
  Flexibly Adapts Capacity to Meet Project Needs​
  Fully Integrated O3 Process Controls & Instrumentation​
  Built-In Multi-Mode Process Control​
  Self-Optimizing Process
MODULAR
The World Most Advanced Ozone Technology
  Zero-Maintenance Ozone Cells​
  +25yr QuadBlock Ozone Cell Life​
  Built-In Redundancy​
  Auto-Compensating Performance​
  100% US Made & Supported
RELIABLE
  Constant 6-18 %BW at Any Output​
  True 0-100% Turn-Down ​
  Industry Leading Power Efficiency​
  Less Cooling​
  Smaller Footprint​
  Ultra-Quiet Operation​
  Built-In Cooling / Heating (no HVAC required)​
  Appliance Like Installation (5 connections)​
  10-40% Lower OPEX and 20yr NPV
RELIABLE
  Onsite Service
24-7 REMOTE & ONLINE SUPPORT
SYSTEM PREVIEW
QuadBlocks in a system

## Slide 7
SYSTEM PREVIEW
QuadBlocks in a system

## Slide 8
Enclosed cabinets
All equipment is on skids
Six (6) connections
    Gas in & out
    Water in & out
    Power compressed air
Easy to install
Air-to-water cooling
Water-to-water cooling
Heat exchanger

## Slide 9
Air-to-water cooling
Water-to-water cooling
Heat exchanger
DIFFERENT OPTIONS
Ozone
Generator Cooling
Air cooling for the electronics
Water cooling for the Dielectrics
Ozone
Cooling

## Slide 10
Air cooling for the electronics
Water cooling for the Dielectrics
Ozone
Cooling
Oxygen Treatment
Manifold
  Donaldson filter
  Demister
  Pressure

## Slide 11
Oxygen Treatment
Manifold
  Donaldson filter
  Demister
  Pressure
Air cooling for the electronics
Water cooling for the Dielectrics
Oxygen Supply
Liquid Oxygen (LOX)
High Purity: Typically >99.5% oxygen
Consistent Supply: Delivered in bulk, stable and continuous ozone production
Low Maintenance: No on-site oxygen generation equipment needed
Applications in Ozone Systems:
Municipal and industrial projects
Ensures optimal performance for ozone generators with minimal operational intervention

## Slide 12
Oxygen Supply
Liquid Oxygen (LOX)
High Purity: Typically >99.5% oxygen
Consistent Supply: Delivered in bulk, stable and continuous ozone production
Low Maintenance: No on-site oxygen generation equipment needed
Applications in Ozone Systems:
Municipal and industrial projects
Ensures optimal performance for ozone generators with minimal operational intervention
Ozone Supply
VSA/PSA (Vacuum/Pressure Swing Adsorption)
On-site systems that extract oxygen from ambient air using molecular sieves
Produce oxygen at 93–95% purity, suitable for ozone generation
Why Use VSA/PSA?
On-Demand Production: No dependency on external oxygen deliveries
Cost-Effective: Lower long-term operational cost for small to mid-size systems
Compact & Modular: Easily integrated into plant layout

## Slide 13
Ozone Supply
VSA/PSA (Vacuum/Pressure Swing Adsorption)
On-site systems that extract oxygen from ambient air using molecular sieves
Produce oxygen at 93–95% purity, suitable for ozone generation
Why Use VSA/PSA?
On-Demand Production: No dependency on external oxygen deliveries
Cost-Effective: Lower long-term operational cost for small to mid-size systems
Compact & Modular: Easily integrated into plant layout
Air-to-water cooling
Water-to-water cooling
Heat exchanger
Ozone Off Gas Destruct Unit

## Slide 14
Ozone Off Gas Destruct Unit
Ozone destruct sizing
Gas production​
Level variation in the tank
Features
Safely removes residual ozone
Catalytic destruction
Compact stainless-steel design
Fits various system sizes
321-506-1850
www.pinnacleozone.com
Cocoa, Florida, USA
Thank You for Attending
We look forward to the journey ahead, where we can turn our shared vision into reality.
  Uses pressure differential to pull in gas or liquid (e.g., ozone)
  High-velocity flow creates suction at the injector throat
  Efficient, reliable mixing with no moving parts
Injection: Venturi

## Slide 15
Injection: Venturi
  Uses pressure differential to pull in gas or liquid (e.g., ozone)
  High-velocity flow creates suction at the injector throat
  Efficient, reliable mixing with no moving parts
Injection
  Side Stream injection
  Venturi mixing
  Dissolution
    Jet nozzle
    Pipe injection
    Ceramic diffusers

## Slide 16
Injection
  Side Stream injection
  Venturi mixing
  Dissolution
    Jet nozzle
    Pipe injection
    Ceramic diffusers
  Evenly distributes ozone into water for maximum contact and efficiency
  Engineered internal design promotes thorough mixing and gas transfer
  Ideal for high-flow applications requiring reliable disinfection or oxidation
OZONE MIXING
Mazzei

## Slide 17
  Evenly distributes ozone into water for maximum contact and efficiency
  Engineered internal design promotes thorough mixing and gas transfer
  Ideal for high-flow applications requiring reliable disinfection or oxidation
OZONE MIXING
Mazzei
OZONE MIXING
Statiflo
Evenly distributes ozone into water for maximum contact and efficiency
Engineered internal design promotes thorough mixing and gas transfer
Ideal for high-flow applications requiring reliable disinfection or oxidation
Injection
  Side Stream injection
  Venturi mixing
  Dissolution
    Jet nozzle
    Pipe injection
    Ceramic diffusers

## Slide 18
OZONE MIXING
Statiflo
Evenly distributes ozone into water for maximum contact and efficiency
Engineered internal design promotes thorough mixing and gas transfer
Ideal for high-flow applications requiring reliable disinfection or oxidation
Maximizes ozone contact time and transfer efficiency in a compact footprint
Engineered for high-flow, high-concentration disinfection processes
Corrosion-resistant materials and rugged frame for long service life
TECHNOLOGY OVERVIEW
Pipe Loop Reactor
  Evenly distributes ozone into water for maximum contact and efficiency
  Engineered internal design promotes thorough mixing and gas transfer
  Ideal for high-flow applications requiring reliable disinfection or oxidation
OZONE MIXING
Mazzei

## Slide 19
Maximizes ozone contact time and transfer efficiency in a compact footprint
Engineered for high-flow, high-concentration disinfection processes
Corrosion-resistant materials and rugged frame for long service life
TECHNOLOGY OVERVIEW
Pipe Loop Reactor
MASTER OPERATOR
CONTROL PANEL (MCOP)
OZONE GENERATOR
  Schneider PLC M251. Allen Bradley available upon request
  HMI Red Lion 15"
EXTERNAL INSTRUMENTATION
  Dissolved O3 residual analysers​
  Ambient O2 and O3 analysers​
  Demister​
  Mass flow controler​
  Dissolved ozone analyser or ORP
Instrumentation & Controls

## Slide 20
Instrumentation & Controls
MASTER OPERATOR
CONTROL PANEL (MCOP)
OZONE GENERATOR
  Schneider PLC M251. Allen Bradley available upon request
  HMI Red Lion 15"
EXTERNAL INSTRUMENTATION
  Dissolved O3 residual analysers​
  Ambient O2 and O3 analysers​
  Demister​
  Mass flow controler​
  Dissolved ozone analyser or ORP
6 Weeks
Up to 22 weeks after approval​
SUBMITTALS
DELIVERY
Project Considerations
Equipment availability and lead-times
Recommended useful Life/mechanical warrantee
Performance warrantee
Output (ppd) warrantee vs MTE

## Slide 21
6 Weeks
Up to 22 weeks after approval​
SUBMITTALS
DELIVERY
Project Considerations
Equipment availability and lead-times
Recommended useful Life/mechanical warrantee
Performance warrantee
Output (ppd) warrantee vs MTE
MASTER OPERATOR
CONTROL PANEL (MCOP)
OZONE GENERATOR
  Schneider PLC M251. Allen Bradley available upon request
  HMI Red Lion 15"
EXTERNAL INSTRUMENTATION
  Dissolved O3 residual analysers​
  Ambient O2 and O3 analysers​
  Demister​
  Mass flow controler​
  Dissolved ozone analyser or ORP

## Slide 22
Thank You for Attending
We look forward to the journey ahead, where we can turn our shared vision into reality.
321-506-1850
www.pinnacleozone.com
Cocoa, Florida, USA